PRELIMIARY DOCUMENT

Pan, Tilt, Zoom (PTZ) Camera Controller	12/10/98

General Description

Uplink

The PC/104 Ground Control Station (GCS)  generates a 10 Hz interrupt.   The joysticks for PAN, TILT, and ZOOM (PTZ) are A/D converted and read during this interrupt.  The A/D counts are converted to a VELOCITY number for the PTZ motor controller.  These numbers are formatted and sent up to the PC/104 PTZ controller using the Uplink Message Format.  The PTZ controller formats the VELOCITIES into a message for the Micro Mo Motor controllers.

A 3 second timeout is used on the uplink. If data is not received by the PTZ Controller within 3 seconds, the PTZ will be instructed to go to the HOME position.

Downlink

The PTZ controller receives the POSITION of the motors for PAN and TILT, and the ZOOM of the camera and sends down these values to the GCS.  The GCS converts the PAN and TILT values to DEGREES using the equation:

degrees = 360 - ((degrees/(535368*4))*360);

The number 535368*4 is the number of motor encoder positions for a 360 degree circle.

The ZOOM is converted to a multiplied factor using the slope of  a line equation:

zoom = (zoom/93) + 1 ;

Data Rate

5 Hz Uplink.  Downlink is synchronized to the uplink.

Message Formats

The uplink and downlink messages are in ASCII.  For example, if PAN_Velocity = 2000,

the data is: 32 30 30 30.  The message is formatted in C using a SPRINTF instruction.  The message parameters are COMMA delimited.

Uplink Message Format

%c,%d,c%,%d,%d,%c

SYNC,Id,Mode,PAN_Velocity,TILT_Velocity,ZOOM_Velocity,EOT

Downlink Message Format

%c,%ld,%ld,%d,%c

SYNC,PAN_Position,TILT_Position,ZOOM_Position,EOT

Variable		Type		Definition

Id			$d		Not defined

Mode			%c		1= NORMAL

2= HOME

PAN_Velocity		%d		+/- 8000

TILT_Velocity		%d		+/- 2500

ZOOM_Velocity		%d		0= Zero

1= Wide Fast

2= Wide Slow

8= Tele Slow

9= Tele Fast

PAN_Position		%ld		+/- 2,141,472

TILT_Position		%ld		-8,350 to 539,000 (Approximate)

ZOOM_Position		%d		0-3FF?

Constant		ASCII		DEC		HEX

SYNC			$		36		24

EOT			EOT		4 		4

COMMA		,		44		2C

MINUS			-		45		2D

0-9			0-9		48-57		30-39

NOTES: